## Slide 1: Director Memorandum 2025-62 Distribution for Review and Discussion – RCSD TDS Management Plan and Agreement with the City of Riverside
July 3, 2025

## Slide 2: Background
What is TDS?
  TDS, or total dissolved solids, refers to the combined content of all inorganic and organic substances dissolved in water, including minerals, salts, and metals, typically measured in parts per million (ppm). (1 ppm = 1 mg/l)
  1 ppm is about 1 grain of sand in a quart of water
Why does TDS matter?
  High TDS can harm aquatic ecosystems, degrade water quality for downstream users, and increase treatment costs.
  A limit is set for the Santa Ana River to protect water supplies, support habitat health, and comply with regional water quality standards.

## Slide 3: TDS Effects on RCSD
RCSD is 100% groundwater reliant and has high ambient TDS, ~491 mg/l
Home and business use increment adds about 250 – 300 mg/l (cleaning agents, personal care products, water softeners, etc.)
Average TDS concentration in effluent ~787 mg/l
Why does this matter?

## Slide 4: TDS Effects on RCSD
Since the 1970’s, the District has partnered with the City of Riverside to provide primary, secondary, and tertiary treatment to 100% of the District’s wastewater.
  District capacity: 3.055 million gallons per day (MGD), current flow ~1.7 MGD
  Note: The District decommissioned its own plant in the 1980’s
City of Riverside owns and operates a regional wastewater treatment plant to treat the flows produced by customers of:
    City of Riverside (80%)
    Jurupa CSD (12%)
    Edgemont CSD (6%)
    Rubidoux CSD (2%)

## Slide 5: TDS Effects on RCSD
City of Riverside holds all regulatory permits, specifically:
  National Pollutant Discharge Elimination System (NDPES) No. CA0105350
    Maximum TDS: 650 mg/l (RCSD ~787 mg/l)
    Based on 12-month averaging
    Year: 2013
    Note: The City of Riverside is working on a new permit with a focus to change the 12-month averaging to 5, 10, 15, or 20 years. Riverside expects to have the permit soon.
Current plant-wide compliance: ~600 mg/l (as the District contributes only 6-8% of the total flow, the District benefits from TDS capacity generated by other partners)

## Slide 6: TDS Effects on RCSD
Why this matters?
  Partners should be independently compliant with regulatory permits (language per existing agreements)
    i.e., RCSD should independently comply with 650 mg/l
  Existing litigation with City of Riverside
    Objection to Rio Vista annexation

## Slide 7: Rio Vista Specific Plan
Mixed land use master planned facility consisting of:
  1,697 residential units
  1.2 million sq. ft. light industrial
  1.4 million sq. ft. business park
  510 acres open space/infrastructure
RCSD impacts:
  $22 million in capacity fees
  $3.2 million in annual utility charges
  $1.2 million in annual prop. tax revenues
  (based on current numbers which will increase over time)

## Slide 8: Rio Vista Specific Plan
Riverside has opposed LAFCO annexation of the Rio Vista Specific Plan (and others) due to:
  Existing TDS effluent not complying with the permit
  Claim new development will exacerbate the existing issue
LAFCO has generally sided with Riverside and would not move the annexation forward until a viable TDS Management Plan could be negotiated and agreed to by both parties
  LAFCO has since completed the annexation under the premise the plan becomes formalized by both organizations.

## Slide 9: Past TDS Efforts
2019: Removal of high-TDS discharger (Aramark) from collection system to Inland Empire Brine Line (IEBL)
  Cost: $450,000 in construction costs and $1,900,000 in returned capacity fees
  TDS: Dropped from ~915 mg/l to current amount, ~787 mg/l
2019: Completion of TDS study identifying contributing sources and mitigation measures
2022: Updates to Water and Sewer Master Plans
2024: 5-party Agreement for low-TDS import water (2,000 AFY)
2024: Completion of 100% design of West Valley WD intertie
Although these efforts were acknowledged, they weren’t enough for Riverside to release their objection. TDS Management Plan

## Slide 10: TDS Management Plan
Started January 2024 – Cooperative effort between RCSD and Riverside
May 2025 - Bilaterial agreement by both staffs
Plan
  Introduction – Provides history of the District, current operations, and TDS issues
  Wastewater Treatment Plant – Describes the origin of the regional plant and partnerships within the plant
  Past TDS Efforts and Alternatives – Describes past District efforts to address TDS (described in previous slide) and other alternatives staff considered to mitigate TDS
  Proposed Plan – Summarized the plan to further mitigate TDS

## Slide 11: TDS Management Plan
Construction of Intertie Infrastructure (2 pathways)
  Rio Vista developer constructs the intertie as a condition of approval (subject to District reimbursement)
  The District constructs the intertie after the 750th new EDU is connected to the District’s system
    Count begins after agreement becomes effective
    Construction must be complete within 12 months of 750th EDU being connected
    Additional considerations:
      District received Notice of Award for $500,000 for construction of the intertie, reduce District cost share
      Constructing now (within 2-3 years) will lower overall cost

## Slide 12: TDS Management Plan
Trigger-Based Blending with Imported Water
  District will purchase low-TDS water in sufficient quantities to individually comply with NPDES permit (650 mg/l)
  Trigger based on NPDES averaging time
  Riverside is working to secure a 10-year averaging period in the upcoming NPDES permit
  Current compliance amount: 600 mg/l
  Trigger amounts developed to provide compliance buffer and is not expected to be exceeded for many years.

## Slide 13: TDS Management Plan
Flexibility for Local Treatment Alternatives
  If the District develops a local TDS treatment solution, like reverse osmosis, capable of achieving compliance independently, the use of imported water may be reduced or discontinued

## Slide 14: Agreement
Supports and effectuates the TDS Management Plan
Preserves all existing contractual arrangements between the agencies and is narrowly focused on TDS Management
Reviewed by General Counsel – John Harper
Reviewed by Special Counsel – Kit Bobko
  Both confirmed its appropriateness in light of ongoing litigation as it is limited in scope to TDS compliance.

## Slide 15: Budget Considerations
No immediate action required.
Drafting of Plan and Agreement accounted for within existing budget for salaries and wages.
Should the District proceed forward with constructing the intertie, staff will return to the Board at a later date for consideration and approval.

## Slide 16: Other Considerations and Next Steps
18-month collaborative effort with Riverside
Narrow focus on complex regulatory issue
Eliminate objections to future annexations
Viable plan, minimizing expedited response and preserving capital
Next steps:
  Board discussion and review
  July 17 – Consideration to adopt

## Slide 17: Recommendation
Staff recommends the Board of Directors:
  Review the TDS Management Plan and Agreement and provide any questions or comments to staff prior to the July 17, 2025, regular Board meeting.

## Slide 18
Rubidoux Community Services District
Office: 951.684.7580
www.rcsd.org
Questions
18